## Slide 1: Digital design of food manufacturing processes – theory and applications
Assoc. Prof. PhD. Ion Dan Mironescu
ULBS
1) The digital materials do not reflect the views of Financial Mechanism Office (FMO), and they do not purport to be representative of the countries, regions and themes they illustrate. The use of the materials does not imply endorsement by the FMO, the Donor States, the Beneficiary States, or any other stakeholder of the EEA and Norway Grants. The FMO is not liable for any law infringements by third parties in the context of the operation and use of the media library.
Modernizing Agricultural Practice using Internet of Things MAPIoT Summer School in Norway 24.07.2022 – 07.08.2022 Melsom High School, Sandefjord organized by University of South-Eastern Norway

## Slide 2: Overview
Introduction to modeling and simulation using Petri Nets | Basic elements: places, transitions , arcs Simulation Modeling concurrency Timed nets Determinism vs stochastic Special arcs
Introduction to modelling and simulation of food manufacturing processes | Modeling processing equipment Modeling transport equipment Modeling control Modeling robots Modeling human operators Modeling a complete manufacturing line Simulating a complete manufacturing line
Introduction to digital design manufacturing processes | Designing the layout Designing the operation of the line Designing the command and control system

## Slide 3: 1. Introduction to modeling and simulation using Petri Nets

## Slide 4: Modelling and simulation
Model - simplified representation of reality
Simulation – uses the model to predict how parts of/ real world evolve
Mathematical models
  Continous time models
    Partial Differential Equation (PDE) from sciences (physics, chemistry, biology)
    Change is continous in time
  Discret event models
    Change only at discret points in time (e.g Petri nets)

## Slide 5: TINA (TIme petri Net Analyzer Toolbox
Toolbox hompage with news, tutorials and software
    https://projects.laas.fr/tina/papers.php
Download software from
    https://projects.laas.fr/tina/binaries/tina-3.7.0-amd64-mswin.zip
Unzip in an appropiate directory
Start (with) the visual editor simulator nd.exe located in the bin subdirectory

## Slide 6: Basic elements: places, transitions , arcs
Place
Place attributes
Transition
tool
Token
Arc
Transition
Place
tool
Arc
tool
Selection
tool

## Slide 7: Simulation
Simulation tool
Input place – pre conditions
Active transition – the input places contain a number of token greater or equal to the weights of the ingoing arcs
Outgoing arc
Ingoing arc
Output place -
If no transition is active, the system has reached his final (dead) state
By clicking on a active transition – the transition fires
A number of token equal to the weight of the ingoing arc (1) is subtracted from the input places.
A number of token equal to the weight of the outgoing arc (1) is added to the output places.

## Slide 8: Simple model – enzymatic reaction

## Slide 9: Simple model – simulation

## Slide 10: Modeling concurrency
Two substrates can interact with the same enzyme – they compete for the active site

## Slide 11: Buffer with limited capacity

## Slide 12: Timed nets
Current simulation time
Manual selection of the next firing time
Time to next firing – deterministic – if the transition remains active, it will fire in 4,15 time units
Time to next firing – stochastic – if the transition can fire now or at any time shorter then 4,15 time units

## Slide 13: Determinism vs stochastic
By manualy firing the transition, a deterministic simulation can be performed – maintaining the same order of firing each time
By runing the automatic simulation a non deterministic simulation can be performed – if two or more transition are active simultaneously the program selects randomly which is fired - the order of firing is not preserved
The player menu can be used to start, stop, rewind, replay step by step any current simulation
port

## Slide 14: Special arcs - Life cycle example
Read arc the transition is active as long as the place contains tokens
The net models a microorganism population through its lifecycle
Inhibitor arc - the transition is inhibiated as long as the place contains tokens
The lower part contains the model of real entities –microorganisms/ substrate/ products
The upper part contains the phases of the lifecycle – each phase controls the processes that are specific

## Slide 15: Multiplication phase
As long as the token is marking the multiplication phase, the multiplying transition is active and the nicroorganism consumes substrate and divide

## Slide 16: Transition to production phase
When no substrate token are available, the transition t0 to the production phases is activated

## Slide 17: Production phase
In the production phase, the producing transition is activated and product tokens are generated

## Slide 18: Transition to death phase
As the number of product token reaches an fixed threshold (30) the transition t1 to death phase is activated

## Slide 19: Death phase
In the death phase, the tokens from the microorganism place are removed by the dying transition

## Slide 20: 2. Introduction to modelling and simulation of food manufacturing processes

## Slide 21: Modeling processing equipment

## Slide 22: Modeling transport equipment
Belts, pipes, conveyors
Manipulator arms
AVG

## Slide 23: Modeling robots

## Slide 24: AGV

## Slide 25: Modeling control
Control loop
  sensors – observable outputs - sensor places
  control unit
  efectors/enablers – controlable inputs – control places or control transitions

## Slide 26: Robotic arm automation

## Slide 27: AVG automatisation
Ion Mironescu, ULBS ©

## Slide 28: Modeling human operators

## Slide 29: Modeling a complete manufacturing line

## Slide 30: Simulating a complete manufacturing line

## Slide 31: 3. Introduction to digital design manufacturing processes

## Slide 32: Line layout

## Slide 33: Petri net model of the line

## Slide 34: Designing the operation of the line - Scheduling
Optimization problem represented by a triple α | β | γ
  α The design of the resources
  β The running properties and constraints
  γ The target function to be maximised or minimised - a combination (weighted sum) of completion time Cj, flow time Fj, Lateness Lj Throughput Uj, Tardiness Tj, Earlisness Ej
is an NP problem for m>2
Intensive researched domain
need intensive mathematical support for solving
But
- modeling can qualitatively help understand and classify the scheduling problem (α | β | γ )
- simulation can qualitatively and quantitatively validates the results and algorithms

## Slide 35: Designing the command and control system

## Slide 36: Recap
Introduction to modeling and simulation using Petri Nets | Basic elements: places, transitions , arcs Simulation Modeling concurrency Timed nets Determinism vs stochastic Special arcs
Introduction to modelling and simulation of food manufacturing processes | Modeling processing equipment Modeling transport equipment Modeling control Modeling robots Modeling human perators Modeling a complete manufacturing line Simulating a complete manufacturing line
Introduction to digital design manufacturing processes | Designing the layout Designing the operation of the line Designing the command and control system